	Gabriel GOSMANN / Felipe LORENZON
École Centrale de Lille / EBE – Electronics for biomedical engineering	June, 2024.

Oscillators
# Part 1 : Theory
1. Give an expression for β(jω).
2. What is the condition on A0 and β(jω) for the circuit to oscillate with a stable amplitude ?
3. Derive :
▪ An expression for oscillation frequency F0.
▪ The condition on R2 et R1 for a constant amplitude oscillation, without clipping.
4. Calculate values for C et R2 so as to obtain a 50 kHz, constant amplitude oscillation.
5. What is its peak-to-peak amplitude. In practice, how can it be varied ?
6. We want the oscillator to operate at frequency Fc, which is not a priori known. What are the values of gain and phase shift induced by the amplifier at this frequency?
7. Derive conditions on R, C and A0 for the circuit to oscillate at constant amplitude, without clipping.
8. The opamp has a GBP of 3 MHz. Calculate values of Fc and C. Now, switch K is open, and the oscillation frequency is the same as in question 4.
9. Plot the current vs. voltage characteristics of one of the diodes D1 or D2.

In the 2 next questions, assume that D1 and D2 are OFF.
10. Give an expression for the gain of the amplifier.
11. Express voltage VR3 (Figure 1.2) vs. Ve.
12. Starting with D1 and D2 OFF, what is the condition on Ve for diode D2 to become ON? What is, then, the state of D1 ?
13. In that cas, redraw the equivalent circuit around the amplifier, and derive a relationship between Vs, Ve and VD0 whrn D2 in ON and D1 OFF.
14. Plot the transfer chacrcateristics Vs = f(Ve) of the amplifier for -15V < Ve < +15V.
15. What is the purpose of diode D1 and D2 ? Please justify your answer.
16. What is the conditions on R3 for the output oscillation to start?
17. Give an expression for output peak amplitude Vsmax vs. VD0, R1 et R2.
# Part 2 : Simulation

## Wien Oscillator
1. Calculate the value of oscillation frequency F0 in Hz and of resistor R2 to maintain a stable oscillation.
2. Simulate the circuit using LTSpice, with UA741 opamp (see homework #1). Take R2 slightly higher than theory. Simulate in ‘Transient’ mode, and choose a sufficient stop time to observe steady-state. To observe the oscillation startup, select « start external voltage supply at 0V »
3. Compare theory with simulation and conclude.
4. We know want the oscillator to operate at the cutoff frequency of the amplifier. Run a simulation to validate the results from question 6 in part I.
## Oscillator with RC phase shifter

1. Using LTSpice, simulate TF βRC ( jω ) = V1 / VS (amplitude and phase) of the RC phase shifter alone, not connected to the amplifer. Note: the RC phase shifter is loaded by R1. which should be included in the circuit schematic.
2. Compare with theory (see slides of the course on Oscillators).
3. Derive frequency F0 in Hz et the value of R2 for stable oscillations.
4. Simulate the circuit of Fig. 2.2 using LTSpice, with UA741 opamp (see homework #1). Take R2 slightly higher than theory. Simulate in ‘Transient’ mode, and choose a sufficient stop time to observe steady-state. To observe the oscillation startup, select « start external voltage supply at 0V »
5. Compare theory with simulation and conclude.
## Amplitude control

1. Using LTSpice, simulate the transfer characteristics VS vs. V1 of the amplifier alone, including diodes (Fig. 2.3). For the purpose, set simulation mode to « DC sweep » corresponding to an input voltage ramp. For the diodes, use the standard model in the LTSpice library.
2. For R2 = 1,5 kΩ, show how the amplitude of VS can be predicted from transfer characteristics.
3. For R2 = 1,5 kΩ, simulate the full Wien oscillator (Fig. 2.2), including diodes.
4. Compare amplitude of Vs obtained from simulation and from the previous question.
5. Compare with theory (question 17), if you have gone that far.