	Gabriel GOSMANN / Felipe LORENZON
École Centrale de Lille / EBE – Electronics for biomedical engineering	May, 2024.

Operational amplifiers (Opamps)
Part 1 : Theory

Exercise 1 : In the circuits of figure 1, calculate the value of the voltage V. Use LTSpice to check your results.

V=8V

V=2V

V = -2V

V = 5V

V = -2V

Exercise 2 : In the circuit in Figure 2, calculate the values of V1 and V2. Use LTSpice to check your results.

V1 = -5V
V2 = 0V

Exercise 3 : The circuit in Figure 3 measures light intensity using a photodiode. The latter, polarized in reverse, produces a current of 0.5uA per uW of incident power. Determine the value of R for which the sensitivity of the conditioner is 0.4mV/mW. Verify your result with LTSpice by replacing the{photodiode, voltage source} assembly with a suitable element.

Here I suppose the sensor is submitted to exactly 1mW of	power.
R = 800 Ohms

Exercise 4 : In the circuit of figure 4, give the expression of Vo as a function of V1 and V2. Under what condition on resistors R1 to R4 is there a differential amplifier?

R3 / R1 = R4 / R2