	Gabriel GOSMANN / Felipe LORENZON
École Centrale de Lille / EBE – Electronics for biomedical engineering	June, 2024.

Oscillators
# Part 1 : Theory
1. Give an expression for β(jω).

For the compontents in paralellel from Vs2 to the ground:

frac{1}{Z_1} = {frac{1}{frac{1}{sC}}} + frac{1}{R} drarrow Z_1 = frac{1}{sC + frac{1}{R}} = frac{R}{1+sRC}
For the components in series from Ve2 to to Vs2
Z_2 = R + frac{1}{sC}
The circuit is a voltage divisor:
V_s2 = {frac{Z_1}{Z_1+Z_2}} cdot V_e2 drarrow frac{V_s2}{V_e2} = frac{frac{R}{1+sRC}}{frac{R}{1+sRC} + R + frac{1}{sC}} drarrow %beta(s) = frac{sRC}{(sRC)^2+3sRC+1}
%beta(j %omega) = frac{j %omega RC}{(1-( %omega RC)^2) + 3j%omega RC}
2. What is the condition on A0 and β(jω) for the circuit to oscillate with a stable amplitude ?

The condition is A_0 cdot %beta(j %omega_0) = 1 . It can further broke down into two simpler conditions:
abs{A_0} abs {%beta(j %omega_0)} = 1
arg(A) + arg(%beta(j %omega)) = 2 %pi n, n in setN
Assuming A is always real, this means that arg(%beta(j%omega)) = %pi n, n in setN

3. Derive :
▪ An expression for oscillation frequency F0.
Plotting the bode diagram for the transferfunction, it is possible to verify that the point of interest is when the phaze is 0, as it never reaches a right angle.

arg(%beta(j%omega)) = 0 drarrow arg(j %omega RC) - arg((1-(j %omega RC)^2)+3 j %omega RC) = 0
{frac{%pi}{2}} - arctan(frac{3 %omega RC}{1-(%omega RC)^2})=0 drarrow frac{3 %omega RC}{1-(%omega RC)^2} rightarrow infinity drarrow 1-(%omega RC)^2 rightarrow 0 drarrow 1 = %omega_0 RC drarrow %omega_0 = frac{1}{RC}
drarrow F_0 = frac{1}{2 %pi RC}
▪ The condition on R2 et R1 for a constant amplitude oscillation, without clipping.
Assuming, as stated, that K is closed, the diodes do not interact wit the circuit. The amplifier is a simple non-inverter, which has a gain as:
A_0 = 1 + frac{R_2}{R_1}
In order to know how much gain is needed, it is necessary to calculate the amplitude at F0.
abs{%beta(j %omega_0)} = abs{frac{j %omega_0 RC}{(1 - (%omega RC)^2) + 3j %omega_0 RC}} = abs{frac{j}{(1-(1)^2) + 3j}} = abs{frac{1}{3}} = frac{1}{3}
drarrow A_0 cdot frac{1}{3} = 1 drarrow A_0 = 3 drarrow 1 +frac{R_2}{R_1} = 3 drarrow R_2 = 2 R_1
4. Calculate values for C et R2 so as to obtain a 50 kHz, constant amplitude oscillation.
It is given that
R_1 = 100 %OMEGA drarrow R_2 = 200 %OMEGA
%omega_0 = frac{1}{RC} = 50 kHZ drarrow C = frac{1}{100 cdot 50 000} = 2e-7 F = 200 nF
5. What is its peak-to-peak amplitude. In practice, how can it be varied ?
Peak-to-peak voltage is the difference between the maximum and the minimum voltages in a signal. It can be varied with another amplification stage after the signal generation, or by changing the supply voltage in the opamp.
6. We want the oscillator to operate at frequency Fc, which is not a priori known. What are the values of gain and phase shift induced by the amplifier at this frequency?
abs{G(j%omega)}=abs{frac{A_0}{1 + j frac{F_c}{F_c}}}= abs{frac{A_0}{1+j}} = frac{A_0}{sqrt{2}} = A_0 cdot frac{sqrt{2}}{2}
arg(G(j%omega)) = arg(frac{A_0}{1+j}) = arg(A_0)- arg(1+j) = 0 - arctan(frac{1}{1}) = - frac{%pi}{4}
7. Derive conditions on R, C and A0 for the circuit to oscillate at constant amplitude, without clipping.
We need to go back to the basic conditions
G(j%omega) %beta(j %omega) = {frac{A_0}{1 + j frac{%omega}{%omega_c}}} cdot frac{j %omega RC}{(1-( %omega RC)^2) + 3j%omega RC}
Phase condition: it must be null
arg(G%beta(j%omega_0)) = 0 drarrow arg(frac{A_0 j %omega RC}{(1 + j frac{%omega}{%omega_c})((1-( %omega RC)^2) + 3j%omega RC)}) = 0
drarrow 0 = {frac{%pi}{2}} - arg((1 + j frac{%omega}{%omega_c})((1-( %omega RC)^2) + 3j%omega RC))
drarrow {frac{%pi}{2}} = arg((1 - (%omega RC)^2-3%omega RC {frac{%omega}{%omega_c}}) + j (3%omega RC + frac{%omega}{%omega_c}(1 - (%omega RC)^2)))
drarrow {frac{%pi}{2}} = arctan(frac{3%omega RC + frac{%omega}{%omega_c}(1 - (%omega RC)^2)}{1 - (%omega RC)^2-3%omega RC {frac{%omega}{%omega_c}}}) drarrow {tan(frac{%pi}{2})} = frac{3%omega_c %omega RC + %omega - %omega^3 R^2 C^2}{%omega_c - %omega_c %omega^2 R^2 C^2-3 %omega^2 RC}
tan(frac{%pi}{2}) rightarrow infinity drarrow the denominator must equal zero, since the numerator is finite
(%omega_c - %omega_c %omega^2 R^2 C^2-3 %omega^2 RC) = 0 drarrow %omega_c = (%omega_c R^2 C^2 + 3 RC) %omega^2 drarrow %omega = sqrt{frac{%omega_c}{%omega_c R^2 C^2 + 3 RC}}
drarrow %omega_0 = frac{1}{sqrt{(RC)^2 + 3 frac{RC}{%omega_c}}}
Note that this formula is equivalent to what was calculated previously, if we assume the opamp is ideal:
%omega_c rightarrow infinity drarrow %omega_0 = frac{1}{sqrt((RC^2) + 0)} = frac{1}{RC}
now, we still need to use amplitude condition, in order to calculate the necessary gain.
abs{G%beta(j %omega_0)} = abs{{frac{A_0}{1 + j frac{%omega_0}{%omega_c}}} cdot frac{j %omega_0 RC}{(1-( %omega_0 RC)^2) + 3j%omega_0 RC}}
1 = {frac{A_0} {abs{ 1 + j frac{%omega_0}{%omega_c}} }} cdot frac{abs{ j %omega_0 RC }}{abs{ (1-( %omega_0 RC)^2) + 3j%omega_0 RC }} drarrow 1 = {frac{A_0} {sqrt{ 1 + frac{%omega_0^2}{%omega_c^2}} }} cdot frac{ %omega_0 RC }{sqrt{ (1-( %omega_0 RC)^2)^2 + 9%omega_0^2 R^2 C^2 }}
drarrow A_0 = frac{sqrt{ 1 + frac{%omega_0^2}{%omega_c^2} } sqrt{ (1-( %omega_0 RC)^2)^2 + 9%omega_0^2 R^2 C^2 }} {%omega_0 RC}
Again, if you assume an ideal opamp, %omega_c >> %omega_0 drarrow A_0 = 3
drarrow A_0 = frac{sqrt{ 1 + frac{1}{(%omega_c RC)^2 + 3 RC%omega_c} } sqrt{ (1-frac{R^2 C^2}{(RC)^2 + 3 frac{RC}{%omega_c}} )^2 + 9frac{1}{(RC)^2 + 3 frac{RC}{%omega_c}} R^2 C^2 }} {frac{RC}{sqrt{(RC)^2 + 3 frac{RC}{%omega_c}}} }
drarrow A_0 = frac{sqrt{ frac{(%omega_c RC)^2 + 3 RC%omega_c+1}{(%omega_c RC)^2 + 3 RC%omega_c} } sqrt{ (1-frac{%omega_c^2 R^2 C^2}{(%omega_c RC)^2 + 3 %omega_c RC})^2 + frac{9 %omega_c^2 R^2 C^2}{(%omega_c RC)^2 + 3 %omega_c RC} }} {frac{RC%omega_c}{sqrt{(%omega_c RC)^2 + 3%omega_c RC}} }
drarrow A_0 = frac{sqrt{ frac{(%omega_c RC)^2 + 3 RC%omega_c+1}{(%omega_c RC)^2 + 3 RC%omega_c} } sqrt{ {frac{(3 %omega_c RC)^2}{((%omega_c RC)^2 + 3 %omega_c RC)^2}} + frac{(3 %omega_c RC)^2}{(%omega_c RC)^2 + 3 %omega_c RC} }} {frac{RC%omega_c}{sqrt{(%omega_c RC)^2 + 3%omega_c RC}} }
drarrow A_0 = frac{3 %omega_c RC sqrt{ (%omega_c RC)^2 + 3 RC%omega_c+1} sqrt{ {frac{1}{((%omega_c RC)^2 + 3 %omega_c RC)^2}} + frac{1}{(%omega_c RC)^2 + 3 %omega_c RC} }} {RC%omega_c}
drarrow A_0 = 3 sqrt{ (%omega_c RC)^2 + 3 RC%omega_c+1} {frac sqrt{{1+ (%omega_c RC)^2 + 3 %omega_c RC}} {(%omega_c RC)^2 + 3 %omega_c RC} }
drarrow A_0 = 3 {frac {{(%omega_c RC)^2 + 3 %omega_c RC + 1}} {(%omega_c RC)^2 + 3 %omega_c RC} } = 3 ( 1 + {frac {1} {(%omega_c RC)^2 + 3 %omega_c RC} }) =3 ( 1 + {frac{1}{%omega_c RC}} {frac{1}{%omega_c RC + 3}} )

8. The opamp has a GBP of 3 MHz. Calculate values of Fc and C. Now, switch K is open, and the oscillation frequency is the same as in question 4.
GBP = 3 MHz drarrow A_0 F_c = 3 cdot 10^6 drarrow A_0 %omega_c = 6 %pi cdot 10^6 drarrow A_0 = frac{6 %pi 10^6}{%omega_c}
frac{6 %pi 10^6}{%omega_c}=3{frac {{(%omega_c RC)^2 + 3 %omega_c RC + 1}} {(%omega_c RC)^2 + 3 %omega_c RC} } drarrow 2 %pi 10^6= {frac {{(%omega_c RC)^2 + 3 %omega_c RC + 1}} {%omega_c (RC)^2 + 3RC} }
drarrow (%omega_c RC)^2 + %omega_c (3RC- 2 %pi 10^6 (RC)^2) + (1 - 6 %pi 10^6 RC) = 0

Using the desired frequency:
2 * %pi * 50 000 = frac{1}{sqrt{(RC)^2 + 3 frac{RC}{%omega_c}}} drarrow (RC)^2 + 3 frac{RC}{%omega_c} = frac {1}{(%pi cdot 10^5)^2} drarrow 3 frac{RC}{%omega_c} = {frac {1}{(%pi cdot 10^5)^2}} -(RC)^2
drarrow %omega_c=frac{3RC}{{frac {1}{(%pi cdot 10^5)^2}} -(RC)^2}
Substituting back into the formula:
( RC frac{3RC}{{frac {1}{(%pi cdot 10^5)^2}} -(RC)^2})^2 + {frac{3RC}{{frac {1}{(%pi cdot 10^5)^2}} -(RC)^2}} (3RC- 2 %pi 10^6 (RC)^2) + (1 - 6 %pi 10^6 RC) = 0
( frac{3R^2 C^2} { {frac {1} {(%pi cdot 10^5)^2} } -(RC)^2 } )^2 + {frac{3RC}{{frac {1}{(%pi cdot 10^5)^2}} -(RC)^2}} (3RC- 2 %pi 10^6 (RC)^2) + (1 - 6 %pi 10^6 RC) = 0
I’m a bit stuck on this.
9. Plot the current vs. voltage characteristics of one of the diodes D1 or D2.
Since the series resistance is assumed to be infinite when ON and zero when off, th graph is just a straight line.
In the 2 next questions, assume that D1 and D2 are OFF.
10. Give an expression for the gain of the amplifier.
The two resistors can be associated in series.
A_0 = 1 + frac{R_2+R_3}{R_1}
11. Express voltage VR3 (Figure 1.2) vs. Ve.
It can be understood as a voltage divisor.
V_E = {frac{R_1}{R_1+R_2}} cdot V_3 drarrow frac{V_3}{V_E}=frac{R_1+R_2}{R_1} = 1 + frac{R_2}{R_1}
As shown before, we already have the output voltage. VR3 is the difference.
V_R3 = V_3 - V_0 = (1 + {frac{R_2}{R_1}} - (1 + frac{R_2+R_3}{R_1}))V_E = -{frac{R_3}{R_1}} cdot V_E
12. Starting with D1 and D2 OFF, what is the condition on Ve for diode D2 to become ON? What is, then, the state of D1 ?
The voltage in the resistor needs to be greater than VDO in the correct orientation. In the case of D2, it means VR3 = -0.6 V. D1 is in reverse polarization and is OFF.
13. In that case, redraw the equivalent circuit around the amplifier, and derive a relationship between Vs, Ve and VD0 when D2 in ON and D1 OFF.
14. Plot the transfer characteristics Vs = f(Ve) of the amplifier for -15V < Ve < +15V.
15. What is the purpose of diode D1 and D2 ? Please justify your answer.
They help stabilize the output. They give a non-linear gain to the amplifier that allows small oscillations to get bigger, but once they are big enough the gain decreases to prevent saturation.
16. What is the conditions on R3 for the output oscillation to start?

17. Give an expression for output peak amplitude Vsmax vs. VD0, R1 et R2.
# Part 2 : Simulation

## Wien Oscillator
1. Calculate the value of oscillation frequency F0 in Hz and of resistor R2 to maintain a stable oscillation.
2. Simulate the circuit using LTSpice, with UA741 opamp (see homework #1). Take R2 slightly higher than theory. Simulate in ‘Transient’ mode, and choose a sufficient stop time to observe steady-state. To observe the oscillation startup, select « start external voltage supply at 0V »
3. Compare theory with simulation and conclude.
4. We know want the oscillator to operate at the cutoff frequency of the amplifier. Run a simulation to validate the results from question 6 in part I.
## Oscillator with RC phase shifter

1. Using LTSpice, simulate TF βRC ( jω ) = V1 / VS (amplitude and phase) of the RC phase shifter alone, not connected to the amplifier. Note: the RC phase shifter is loaded by R1. which should be included in the circuit schematic.
2. Compare with theory (see slides of the course on Oscillators).
3. Derive frequency F0 in Hz et the value of R2 for stable oscillations.
4. Simulate the circuit of Fig. 2.2 using LTSpice, with UA741 opamp (see homework #1). Take R2 slightly higher than theory. Simulate in ‘Transient’ mode, and choose a sufficient stop time to observe steady-state. To observe the oscillation startup, select « start external voltage supply at 0V »
5. Compare theory with simulation and conclude.
## Amplitude control

1. Using LTSpice, simulate the transfer characteristics VS vs. V1 of the amplifier alone, including diodes (Fig. 2.3). For the purpose, set simulation mode to « DC sweep » corresponding to an input voltage ramp. For the diodes, use the standard model in the LTSpice library.
2. For R2 = 1,5 kΩ, show how the amplitude of VS can be predicted from transfer characteristics.
3. For R2 = 1,5 kΩ, simulate the full Wien oscillator (Fig. 2.2), including diodes.
4. Compare amplitude of Vs obtained from simulation and from the previous question.
5. Compare with theory (question 17), if you have gone that far.